Docker Security
Docker
Host → Container
How to allow container to have the least possible permissions and access to the host in order to achieve isolation.

---
AppArmor
Running the image with an AppArmor profile enforced, we can isolate the host as much as we want for each task.
AppArmor profiles have rules that can restrict access of the running image to the host.

---
AppArmor
AppArmor profile:
- Match rule → allow
- No matching rule → deny
  The more specific the profile is, the more strict it will be.

---
AppArmor
AppArmor profile:
1. Static Analysis
2. Dynamic Analysis

---
Static Analysis
A parser that extracts some first permissions on container out of
- Dockerfile
- .yml file (DockerCompose)

---
Static Analysis
Dockerfile
A recipe that tells Docker how to create the image for the container.

---
Dockerfile
- Mount: RUN mount dir & VOLUME /foo
- Network: EXPOSE ports
- Chmod: RUN chmod file
- Chown: RUN chown file

---
Dockerfile
- Mount: RUN mount dir & VOLUME /foo
- Network: EXPOSE ports
- Chmod: RUN chmod file
- Chown: RUN chown file
Mount is a privileged operation and for portability issues
privileged operations are not allowed at the build phase,
only at the runtime phase. For portability reasons again,
we cannot expose certain ports at the build phase either.

---
DockerCompose
DockerCompose gives us parameters that should be given at runtime at docker, all included in a .yml file.

---
DockerCompose
- Network: ports
- Mount: volumes, volume_driver
- Capabilities: cap_add, cap_drop
- Devices: devices
- Resources: cgroup_parent, resources, ulimits (?)

---
AppArmor rules
Dockerfile
- Chmod rule
- Chown rule +
  Chown capability
DockerCompose
- Ports:
  Capability net_bind_service +
  network bind x to y
- Volumes:
  mount [<src>] [ → <mntpnt> ]
- Capabilities add/drop:
  capability x / deny capability x
- Devices rule ???
- Resources, ulimits, cgroup_parent:
  rlimit <rlimit> <= <value>

---
AppArmor rules
1. Chmod & Chown rules:
Το Dockerfile φτιάχνει το image.
Μετά όμως, πρέπει να επιτρέψουμε στο container να έχει αυτό το permission?
Αν ναι, με την ίδια λογική, μήπως πρέπει να προσθέσουμε και για τις εντολές COPY και ΑDD access στο source με read και στο destination με write?
Aντίστοιχα και για WORKDIR path → path με write permission

---
AppArmor rules
2. Ports:
network [domain] [type] [protocol]
Για τα ports θεώρησα ότι χρειάζεται το capability net_bind_service (το είδα και σε έτοιμα profiles στα οποία το application είχε χρήση ports) και network bind x to y (δεν το έχω δει σε κάποιο profile)

---
AppArmor rules
3. Volumes:
Mount rule:
mount [<src>] [ → <mntpnt> ]
Δεν νομίζω ότι χρειάζεται κάποιο capability.
Ίσως access στα paths των src και mntpnt?
(write access και στα δυο)

---
AppArmor rules
4. Capabilities:
- cap_add x: capability x
- cap_drop x: deny capability x
- ALL: Βάζω όλη τη λίστα των capabilities τα οποία υποστηρίζει τώρα το AppArmor.
  3 μόνο δεν υποστηρίζει σύμφωνα με το documentation: syslog, wake_alarm, audit_read τα οποία αγνοεί ο parser

---
AppArmor rules
5. Devices: match device host to device container
Δεν βρήκα κάποιο rule που να αφορά τα devices.
Σκέφτηκα να τα προσθέσω με mount rule, με paths τα paths των devices.
Είναι όμως η σχέση των device σαν mount?

---
AppArmor rules
6. Resources: cgroup_parent, ulimits, resources
rlimit rule: rlimit <rlimit> <= <value>
Μας αφορά για το isolation?

---
Static Analysis
We encourage users to create a .yml Compose file even for a single service - task – so that the parser can extract rules before the dynamic analysis.

---
Dynamic Analysis
To enrich our profile we use AppArmor complain mode:
Profiling
- By hand
- By tools
  with aa-complain

---
Dynamic Analysis
- Create a preliminary profile (static analysis) / Start aa-genprof in a terminal
- Put the profile into complain mode with aa-complain
- Execute test plan (start, stop, commands)
- Monitor the logs
- Adjust the profile
- Put the profile into enforce mode with aa-enforce

---
Dynamic Analysis
- Create a preliminary profile (static analysis) / Start aa-genprof in a terminal
- Put the profile into complain mode with aa-complain
- Execute test plan (start, stop, commands)
- Monitor the logs
- Adjust the profile
- Put the profile into enforce mode with aa-enforce
Τρέχουμε το container με ένα αντιπροσωπευτικό workload. Όπως???